## Slide 1
AudioCodes SBC Deployment Options
Decision Pack
Microsoft Teams Direct Routing - SBC HA Architecture Options
Date: 5 March 2026
Audience: IT Manager, Cybersecurity, Cloud Platform, Voice Engineering
Source: AudioCodes SBC - Unified Deployment & Configuration Guide v2.6
Purpose: Present five SBC deployment options with recommendation
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- Direct Routing: Microsoft Teams feature connecting to PSTN via SBC
- Mediant VE: AudioCodes virtual SBC appliance for cloud/hypervisor deployment

## Slide 2
1. The Problem
A cybersecurity review identified that ec2:ReplaceRoute - the AWS API used by AudioCodes SBCs for internal VIP failover - cannot be scoped to individual route entries. The SBC IAM policy is already at maximum IAM granularity (specific route table ARN + Env tag), but a compromised SBC could still replace any route in that table, not just VIP routes.
Two Failover Paths - Only One Is Affected
 | Internal (VIP) | External (EIP)
Failover API | ec2:ReplaceRoute | ec2:AssociateAddress
What moves | Route table entry to standby ENI | EIP to standby WAN ENI
Connects to | Downstream SBCs, PBX, SIP providers | Microsoft Teams
IAM scoping | Route table ARN + Env tag | EIP ARN + App + Env tags
Concern | Cannot restrict to specific routes | No concern - scoped to single EIP
Key Points
External EIP path (ec2:AssociateAddress) is not affected - already scoped to specific EIP with dual tag conditions
Exploiting this requires the SBC instance to be compromised first - not an internet-facing attack surface
Blast radius bounded to a single route table in a single tagged environment
AWS has confirmed there are no condition keys for destinationCidrBlock or networkInterfaceId on ReplaceRoute
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- ec2:ReplaceRoute: AWS API action to modify a VPC route table entry
- ec2:AssociateAddress: AWS API action to assign an Elastic IP to an instance
- CloudTrail: AWS service recording API calls for auditing
- ARN: Amazon Resource Name - unique identifier for AWS resources
- Route Table: AWS networking construct directing traffic between subnets

## Slide 3
Option 1 - HA with Retrospective Guardrails
RECOMMENDED
Aspect | Detail
Architecture | 1+1 Active/Standby across two AZs - standard AudioCodes HA via Stack Manager
Failover | SBC firmware calls AWS APIs directly; VIP + EIP move to standby; active calls survive
IAM permissions | ec2:ReplaceRoute + ec2:AssociateAddress - both retained
Security controls | 4-layer compensating control architecture (see right)
Exposure window | ~7-18 seconds from malicious API call to full automated containment
Guardrail cost | ~$6/month per region
Licensing | 1x session/feature licence (single logical SBC) + 2x base VM licences
Infrastructure | 2x SBC instances + 1x Stack Manager (t3.medium) per environment
Compensating Controls (4 Layers)
Dedicated VIP route table - only VIP routes in the table; blast radius limited to VIP entries only
EventBridge + Lambda containment gate - validates every ReplaceRoute call; auto-reverts, strips IAM, quarantines, alerts
Scheduled canary Lambda - polls route table every 60s against VIP allowlist; independent backstop
AWS Config + VPC Flow Logs - custom Config rule flags non-VIP entries; Flow Log anomaly detection
Why reactive, not preventive: AudioCodes firmware calls the EC2 API directly during failover - proprietary behaviour that cannot be intercepted
Containment posture: Deny-by-default, fully automated, no human gate. Compromised instance left running in quarantine for forensics
Cost breakdown: Containment Lambda ~$1, canary ~$1, provisioned concurrency ~$3, CloudWatch logs ~$1, EventBridge/SSM/SNS/SG = free tier
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- EventBridge: AWS serverless event bus for routing events to targets
- Lambda: AWS serverless compute service that runs code in response to events
- SSM Parameter Store: AWS service for storing configuration data and secrets
- CloudWatch: AWS monitoring and observability service
- SNS: Simple Notification Service - AWS managed messaging service
- Provisioned Concurrency: Lambda feature eliminating cold start latency
- AWS Config: Service for assessing, auditing, and evaluating AWS resource configurations
- VPC Flow Logs: Feature capturing IP traffic information for VPC network interfaces
- Stack Manager: AudioCodes management VM for deploying SBC HA stacks via CloudFormation

## Slide 4
Option 2 - Standalone SBC (No HA)
NOT RECOMMENDED
Aspect | Detail
Architecture | Single SBC instance per region - no HA pairing, no VIP, no route table manipulation
Failover | None - manual recovery (instance restart/replacement)
IAM permissions | ec2:ReplaceRoute removed entirely; ec2:AssociateAddress not required
Security controls | N/A - no IAM risk to mitigate
Single point of failure | Yes - SBC failure = total voice outage for region
Licensing | 1x SBC licence per region
Infrastructure | 1x SBC instance per region; no Stack Manager required
Key Concerns
TOTAL REBUILD for future HA - most likely required at project completion. Kapila (AudioCodes) confirmed standalone to HA is a complete tear-down and rebuild
Stack Manager must deploy the HA pair from scratch via CloudFormation - cannot retrofit HA onto existing standalone instance
Recovery time on failure: minutes to hours. Could extend up to a day if the MSP needs to familiarise with a complex SBC recovery procedure
All active calls drop on instance failure
Fastest path to production - but paints the organisation into a corner
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- CloudFormation: AWS infrastructure-as-code service for provisioning resources
- Stack Manager: AudioCodes management VM required for HA deployment (not standalone)

## Slide 5
Option 3 - Non-Seamless HA (2x Standalone SBCs)
Aspect | Detail
Architecture | Two independent SBC instances per region - not an AudioCodes HA pair
Failover | External: DNS-based, SIP proxy primary/secondary, or Teams DR priority/weight settings
IAM permissions | ec2:ReplaceRoute removed entirely; ec2:AssociateAddress removed entirely
Security controls | N/A - no IAM risk to mitigate
Call survivability | Active calls on primary drop - no session state synchronisation
Licensing | 2x SBC licence per region (double cost)
Infrastructure | 2x SBC instances per region; no Stack Manager required
Key Considerations
Eliminates all route table and EIP IAM permissions - noted IAM risk not present
HA mechanism does not programmatically manipulate the AWS route table - no concerns with this approach
Failover speed depends on DNS TTL or SIP retry timers - not seamless like true HA
Each SBC maintains independent configuration - risk of configuration drift (ongoing operational burden)
Not an AudioCodes-supported HA pattern - this is a custom resilience design
Requires SIP provider and Microsoft coordination for primary/secondary configuration
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- DNS Failover: Using DNS record changes to redirect traffic to a backup system
- Configuration Drift: Divergence between configurations of systems meant to be identical
- Teams DR Priority/Weight: Microsoft Teams Direct Routing settings controlling SBC preference

## Slide 6
Option 4 - On-Premises SBC in HA (Physical)
ALTERNATIVE FALLBACK
Aspect | Detail
Architecture | Physical AudioCodes Mediant appliance (800/1000/2600) with VRRP or native HA
Failover | Traditional HA - VRRP/AudioCodes native; active calls survive
IAM permissions | N/A - no cloud IAM involved
Security controls | Physical security, network ACLs - shifts to physical access domain
Call survivability | Active calls survive (session state synchronised)
Licensing | Hardware appliance licence
Infrastructure | Physical appliance + rack space + power + cooling
Key Considerations
Proven HA mechanism with no cloud API dependency - noted IAM risk not present
Against cloud-first strategy - moves voice infrastructure back on-premises
Hardware procurement lead time: weeks to months depending on model and availability
Requires physical data centre presence with rack space, power, cooling, and network connectivity
Ongoing hardware maintenance and lifecycle management (patching, warranty, end-of-life)
Security concerns shift entirely from IAM/cloud to physical access controls and network segmentation
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- Mediant 800/1000/2600: AudioCodes physical SBC appliance models
- Rack-and-Stack: Physical installation of hardware in a data centre rack

## Slide 7
Option 5 - On-Premises Virtualised SBC in HA
PREFERRED FALLBACK
Aspect | Detail
Architecture | AudioCodes Mediant VE (Virtual Edition) on existing on-premises hypervisors in HA
Failover | Traditional HA - VRRP/native AudioCodes HA on hypervisor; active calls survive
IAM permissions | N/A - no cloud IAM involved
Security controls | Existing on-premises security controls, hypervisor access controls, network ACLs
Call survivability | Active calls survive (session state synchronised)
Licensing | Mediant VE software licence (session/feature + base VM)
Infrastructure | 2x VMs on existing hypervisors - no new hardware procurement
Key Considerations
Same Mediant VE software as the AWS deployment but hosted on existing on-premises hypervisors (VMware, Hyper-V, KVM)
No hardware procurement lead time - uses existing hypervisor capacity, significantly faster than Option 4
No new rack space, power, or cooling required - leverages existing data centre infrastructure
Full AudioCodes HA support - same HA mechanism as Option 4 but virtualised
Noted IAM risk not present - no cloud IAM permissions involved in failover
Against cloud-first strategy - same strategic trade-off as Option 4, but lower capital cost and faster deployment
Dependent on existing hypervisor capacity and availability in required data centre locations
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- Mediant VE: AudioCodes Mediant Virtual Edition - software SBC for hypervisors
- Hypervisor: Software creating and managing virtual machines (VMware, Hyper-V, KVM)
- KVM: Kernel-based Virtual Machine - Linux virtualisation technology

## Slide 8
3. Comparison Matrix
Category | Opt 1: HA + Guardrails | Opt 2: Standalone | Opt 3: 2x Standalone | Opt 4: On-Prem Physical | Opt 5: On-Prem Virtual
HA capability | Full 1+1 Active/Standby | None | External failover (DNS/SIP) | Full HA (VRRP/native) | Full HA (VRRP/native)
Call survivability | Active calls survive | All calls drop | Active calls drop | Active calls survive | Active calls survive
Recovery time | Seconds (automatic) | Mins-hours, up to a day | Secs-mins (DNS/SIP) | Seconds (automatic) | Seconds (automatic)
Security risk | 7-18s window, 4-layer defence | Noted IAM risk not present | Noted IAM risk not present | Noted IAM risk not present | Noted IAM risk not present
Build effort | Moderate-high | Low (fastest) | Moderate | Variable (hardware) | Moderate - existing infra
Licensing | 1x session/feature + 2x base VM + ~$6/mo | 1x SBC/region | 2x full SBC/region | Appliance licence | VE software licence
Future flexibility | Already at target state | Total rebuild for HA | Already HA - no concerns | Locked to on-premises | Locked to on-premises
Vendor support | AudioCodes-supported HA | Standard support | Custom pattern | Hardware support | AudioCodes-supported HA
Cyber approval | Depends on risk appetite | High likelihood | High likelihood | High likelihood | High likelihood
Cloud-first aligned | Yes | Yes | Yes | No | No
Timeline to deploy | Moderate | Fastest | Moderate | Slowest | Moderate-fast
Options 1, 4 and 5 provide seamless failover with call survivability. Options 2 and 3 do not. Option 2 recovery could extend up to a day if the MSP needs to familiarise with a complex SBC recovery procedure. Choosing standalone (Option 2) now and needing HA later = total rebuild (AudioCodes confirmed).
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network

## Slide 9
4. Recommendation
RECOMMENDED
Option 1 - HA with Retrospective Guardrails
Delivers target-state HA architecture from day one. Avoids future rebuild risk. Seamless failover with call survivability. 7-18 second exposure window bounded by 4-layer automated defence. Guardrail cost ~$6/month per region.
PREFERRED FALLBACK
Option 5 - On-Premises Virtualised HA
If Cyber rejects compensating controls and ec2:ReplaceRoute must be eliminated entirely. Full HA, call survivability, noted IAM risk not present. Uses Mediant VE on existing hypervisors - no hardware procurement. Trade-off: depends on cloud-first commitment.
ALTERNATIVE FALLBACK
Option 4 - On-Premises Physical HA
Same outcome as Option 5 using physical Mediant appliance. Use if hypervisor capacity not available. Slowest to deploy due to hardware procurement and data centre logistics.
ALSO CONSIDER
Option 3 - 2x Standalone SBCs
Removes all IAM permissions. HA mechanism does not manipulate AWS route table. Active calls drop on primary failure. Configuration drift risk - each SBC maintains independent config. Ongoing operational burden.
NOT RECOMMENDED
Option 2 - Standalone (No HA)
Single point of failure. Total rebuild required for future HA (most likely at project completion). Recovery could take up to a day. Paints the organisation into a corner.
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- Configuration Drift: Divergence between configurations of systems meant to be identical
- Cloud-first: Organisational strategy prioritising cloud over on-premises deployment

## Slide 10
5. Decision Framework and Next Steps
Factors to Score
# | Factor | Key Question
1 | Risk appetite | Is a 7-18s exposure window with automated containment acceptable, or must ReplaceRoute be eliminated entirely?
2 | Voice criticality | What is the acceptable RTO for voice services? Is a single point of failure tolerable?
3 | Cloud-first commitment | Does cloud-first strategy preclude an on-premises SBC?
4 | Build vs. rebuild | Is the risk of a total rebuild later (Option 2) acceptable given timeline pressures?
5 | Cyber's position | What is the formal position on compensating controls (Option 1)?
6 | Timeline pressure | How urgently must Direct Routing be in production?
7 | Licensing budget | Is double SBC licensing (Options 1 & 3) within budget?
Open Questions for the Decision Meeting
# | Question | Owner
1 | What is the formal position on the 7-18s exposure window with 4-layer automated containment? | Cybersecurity
2 | Is the compensating control architecture sufficient to close the finding? | Cybersecurity
3 | If Option 1 is rejected, is the position permanent or reviewable after non-prod demonstration? | Cybersecurity
4 | What is the acceptable RTO for voice services? | IT Management
5 | Is the total rebuild risk (Option 2 to HA) acceptable? | IT Management
6 | Does cloud-first strategy rule out Options 4 and 5? | IT Management
7 | What is the estimated effort to build the guardrail stack (Option 1)? | Cloud Platform / TTO
8 | Can the guardrail stack be built and tested in non-prod before a final decision? | Cloud Platform / TTO
9 | Can regional SIP providers support primary/secondary SBC config (Option 3)? | Voice Engineering
10 | Is there sufficient hypervisor capacity on-premises for Option 5? | Infra / Voice Eng
11 | What is the hardware lead time for a physical AudioCodes appliance (Option 4)? | Voice Engineering
12 | What is the target date for Microsoft Teams Direct Routing go-live? | All stakeholders
13 | Is this decision per-region or must it be consistent across all regions? | All stakeholders
Notes: GLOSSARY OF TERMS:
- SBC: Session Border Controller - network device managing VoIP sessions at network boundaries
- HA: High Availability - architecture eliminating single points of failure
- VIP: Virtual IP - floating IP address that moves between HA pair members during failover
- EIP: Elastic IP - AWS static public IP address
- IAM: Identity and Access Management - AWS permission and access control framework
- VPC: Virtual Private Cloud - isolated virtual network in AWS
- ENI: Elastic Network Interface - virtual network card attached to an EC2 instance
- AZ: Availability Zone - physically separate data centre within an AWS region
- VRRP: Virtual Router Redundancy Protocol - standard protocol for automatic IP failover
- RTO: Recovery Time Objective - maximum acceptable downtime after a failure
- MSP: Managed Service Provider - third-party IT operations partner
- TTO: Technology Team Operations - internal cloud platform team
- SIP: Session Initiation Protocol - signalling protocol for voice/video sessions
- DNS TTL: Domain Name System Time To Live - cache duration for DNS records
- PSTN: Public Switched Telephone Network - traditional telephone network
- Cloud-first: Organisational strategy prioritising cloud over on-premises deployment
- Go-live: Point at which a system enters production use